# 4th Meeting of the LHC Beam Cleaning Study Group 7.11.2001

Present:	R. Assmann (chairman), H. Burkhardt, G. Burtin, B. Dehning, C. Fischer, E. Gschwendtner, J.B. Jeanneret, R. Jung, V. Kain, R. Schmidt, J. Wenninger

### LHC Orbit Feedback (J. Wenninger)

J. Wenninger presented a detailed study of the LHC orbit feedback. The presentation is appended in the PDF version of the minutes and is available on our web site. Jörg pointed out that the cold correctors are too slow for a fast feedback. They can run at a maximum of 1 Hz. The warm correctors are much faster, allowing to run at 10 Hz, maybe at 20 Hz (they ramp to full current in about 0.5 s). Taking into account the orbit smapling (10 Hz) and the response delays (up to 125 ms) a global orbit feedback with 0.2-0.5 Hz can be envisaged. A local feedback could run at about 1 Hz, if needed. The bandwidth could be increased to 5-10 Hz by installing more warm correctors, by increasing the orbit sampling (to 20 Hz), and by reducing the delays in response. Jörg pointed out that the need fro such a fast feedback should be demonstrated. He calculated the effect from snapback of random B1. The resulting orbit change of 1 mm can be corrected by 900 nrad rms kicks. There is no shortage of corrector strength.

Further questions on orbit stability were discussed, centering on high frequencies (e.g. motion at 50 Hz), the time-dependent orbit during snapback, and the interaction of local orbit feedbacks with the machine protection requirements of the collimation system.

### Preliminary Beam Loss Studies (V. Kain)

V. Kain presented her first results on beam loss studies, done together with R. Schmidt as a technical student. The presentation is appended in the PDF version of the minutes and is available on our web site. Verena introduced the physic implemented in her tracking program. The program allows tracking of a beam distribution in 1D during a magnet quench. Verena showed that, depending on the time scales, the particles must be tracked or an adiabatic change of orbit can be assumed. She calculated the maximum orbit distortion for quenching of different dipoles, showing that the orbit can reach 9.5  for certain phase advance conditions.  This means that the collimation system does protect efficiently against adiabatic orbit changes in one phase, however, not in the orthogonal phase. Further work is required.

### Survey, Collective Effects and Thermal Studies (J.B. Jeanneret)

J.B. Jeanneret reported on three meetings. The presentation is appended in the PDF version of the minutes and is available on our web site. A meeting with J.P. Quesnel, C. Fischer and himself addressed the survey and mounting accuracy for the collimators. The initial survey accuracy will be 150 m, degrading to 200 m after one year of operation. J.B. Jeanneret also had a meeting with D. Brandt and L. Vos on collective effects. A tapering will be needed, adding about 0.2 m to the length of the jaws (0.2 m primary, 0.5 m secondary). This will require a change in the layout of the cleaning insertions. An RF contact might be needed on the collimator jaws. L. Vos and D. Brandt also questioned the vacuum ports on the collimator tank. Further work is required. Finally, J.B. Jeanneret reported on a meeting with T. Kurtyka, R. Valbuen, C. Fischer, R. Jung, and himself. They discussed possible support on thermal studies for the collimators. There was no result and further discussions are needed.

### 4)  Next meeting

The next meeting remains to be announced, due to the BI review on November 19th.